Sorbent property
tot CaCO3Powder mass (g)	total CaCO3 powder in Calciner
250-212 µm CaCO3Powder mass (g)	Mass of CaCO3 powder diameter over 212 µm in Calciner
212-150 µm CaCO3Powder mass (g)	diameter 212-150
150-125 µm CaCO3Powder mass (g)	diemeter 150-125
125-63 µm CaCO3Powder mass (g)
63-<63 µm CaCO3Powder mass (g)	diameter less than 63
tot CaCO3Pellet _mass_(g)	total CaCO3 pellet in Calciner
<-710 µmPellet _mass_(g)
710-600 µmPellet _mass_(g)
600-500 µmPellet _mass_(g)
500-425 µmPellet _mass_(g)
425-355 µmPellet _mass_(g)
355-300 µmPellet _mass_(g)
300-250 µmPellet _mass_(g)
250-212 µmPellet _mass_(g)
212-150 µmPellet _mass_(g)
150-63 µmPellet _mass_(g)
63-> µmPellet _mass_(g)	diameter less than 63 I use wrong < here
tot HBr_CaC03_mass_(g)	total CaCO3 doped with HBr in calciner
<-710 µmHBr_CaC03_mass_(g)
710-600 µmHBr_CaC03_mass_(g)
600-500 µmHBr_CaC03_mass_(g)
500-425 µmHBr_CaC03_mass_(g)
425-355 µmHBr_CaC03_mass_(g)
355-300 µmHBr_CaC03_mass_(g)
300-250 µmHBr_CaC03_mass_(g)
250-212 µmHBr_CaC03_mass_(g)
212-150 µmHBr_CaC03_mass_(g)
150-63 µmHBr_CaC03_mass_(g)
63-> µmHBr_CaC03_mass_(g)
Calciner condition
Calciner temp [°C]	temperature inside calciner
Calciner Heater kW	Heat input to calciner
Calciner Pressure ( Pa )	Calciner pressure
Calciner velocity (m/s)	velocity of fluidized gas in calciner
Calciner CO2 in(%vol)	composition of fluidized gas
Calciner O2 in(%vol)
Calciner N2 in(%vol)
Output from calciner
Calciner top temp ( °C )	temperature of the discharged gas
Calciner CO2 out(%)	composition of discharged gas
Calciner CO out(ppm)
Calciner CH4 out(ppm)
Calciner O2 out(%)
Calciner H2O out(%)
Run status	Ops condition for Calciner / -SU=start up (heating) / -C=calcination / -CC=calcination and carbonation / -CD=cooldown
Carbonator ops condition
Carbonator bottom temp ( C)	temperature in the bottom
Carbonator mid temp ( C)	temperature in the middle
Carbonator press (pa)	pressure
Carbonator velocity (m/s)	gas velocity entering from below
Carbonator inlet CO2 (%vol)	composition of inlet gas
Carbonator inlet N2 (%vol)
carbonator output
Carbonator top temp ( C)	exit gas temperature
Carbonator outlet CO2 (%vol)	composition of exit gas